## Slide 1: pyfluv
A Python package for stream analysis
Sky Jones
Sky.Jones@kci.com

## Slide 2: What is pyfluv?
pyfluv is a free and open source Python package that provides a high level programmatic interface for interacting with geomorphological stream surveys
(and other restoration-related data)

## Slide 3: Goals of pyfluv
Provide a high level, extensible programming library for analyzing stream surveys, with a focus on stream restoration
Encourage standardized data formatting and facilitate the analysis of large amounts of data
  e.g., meta-analyses, remotely sensed data
Demonstrate novel techniques for stream analysis

## Slide 4: Benefits of programmatic analysis
Repeatability and precision
  Document every step of analysis from raw data to final results
Automation
  Create scripts that instantly analyze field data
  Write routines to analyze large amounts of remotely sensed data
Image: WA-DNR

## Slide 5: Downloading pyfluv
Anyone with Python can pip install pyfluv from the terminal
Source code available at https://github.com/rsjones94/pyfluv

## Slide 6: A short demonstration Full tutorials at https://github.com/rsjones94/pyfluv-notebooks

## Slide 7: Reading in a survey
The survey contains
  1516 points
  14 cross sections
  6 longitudinal profiles

## Slide 8: Quickplotting

## Slide 10: Extracting statistics
CrossSections
  Area
  Width
  Hydraulic radius
  Shear stress
  Shear velocity
  Stream power
  Flood prone elevation
  Entrenchment ratio
  Mean and max depth
  Flow velocity
  Discharge rate
  Width/depth ratio
  Froude number
  Bank slopes*
Profiles (and Features)
  Feature spacing
  Sinuosity
  Length
  Slopes (water, bankfull, etc.)
  Max depth
  Planform geometry*

## Slide 11: Profile modification
Interpolating Features
Repairing slopes

## Slide 12: CrossSection modification

## Slide 13: Other features
Rating curve generation*
Profile interpolation and smoothing
Trendline fitting
Grain size analysis
  dX particle size
  Sorting, skewness, kurtosis
  Plotting
Reference reach analysis
  Lines of best fit
  Confidence intervals
  Plotting

## Slide 14: Predictive algorithms
Algorithms meant to facilitate the analysis of stream data that is lacking field callouts and cannot be manually inspected
  Large amounts of remotely sensed data
  Meta-analyses that include data with irregularly formatted/inconsistent callouts

## Slide 15: Predictive algorithms
Top of bank identification
  Find the elevation of maximum flow release in a cross section
Substrate differentiation*
  Identify the points in a cross section where channel substrate transitions to channel bank
Feature classification
  Identify pools and riffles in a profile based on water slope and depth
Breakpoint detection*
  Split a profile into multiple profiles based on changes in profile statistics

## Slide 16: Top of bank identification
Can be estimated as the point where a key derivative is maximized
  1st derivative of hydraulic radius with respect to elevation
  2nd derivative of width with respect to elevation
  3rd derivative of area with respect to elevation

## Slide 17: Substrate differentiation
Most channels can be approximated by 3-5 points**
The outermost line segments represent channel banks
**Optimal solution to this problem is very slow

## Slide 18: Feature classification
Riffles and pools have distinct morphological signatures
Use k-means algorithm to distinguish between them

## Slide 19: pyfluv benefits
Faster turnaround of stream surveys
More accurate and repeatable analyses
Modular, easily extendable framework
Totally free

## Slide 20: Questions